## Slide 1
5g_fuzzer
Config &conf = StateMachine.config;
…
Monitors MonitorTarget = new Monitors();
…
If(MonitorTarget.setup(conf)){
MonitorTarget.SetCallback(log_monitor_program_str);
MonitorTarget.SetCrashCallback(monitor_crash_callback);
MonitorTarget.init(conf);
MonitorTarget.printStatus(); (here to print the status of the device)
}
…
log_monitor_program_str() : only fancy log setup
monitor_crash_callback() : AnomalyReport.IndicateCrash(format("[Crash] Crash detected at state \"{}\"", StateMachine.GetCurrentStateName()));
5gnr_gnb_config.json
"Monitor": {
"Enable": true,
"PrintToStdout": true,
"WaitExternalEvent": false,
"ActiveMonitorTypes": [
3 (only corresponds to ADB used in switch)
],…
"ADB": {
"ADBDevice": "UWEUW4XG8XCA8PWS",
"ADBFilter": "",
"ADBMagicWords": [
"ModemEvent: modem_failure",
"ModemRestartStats",
"SOC crashed",
"Unable to wake SOC"
],
"ADBProgram": "logcat",
"ADBSubSystem": "radio,crash,system,main"
}
Monitors.hpp
setup(conf):
If ADB new MonitorADB();
ADB.SetCallback(log_monitor_program_str);
ADB.SetCrashCallback(monitor_crash_callback);
ADB.init(conf);
printStatus();
MonitorADB.hpp
string *Device = nullptr;
string *Program = nullptr;
string *Filter = nullptr;
string *SubSystem = nullptr;
std::vector<std::string> device_list;
std::string adb_buffer = "";
vector<string> *MagicWords;
ProcessRunner ADBProcess;
function<void(string)> UserCallback = nullptr;
function<void(bool)> UserCrashCallback = nullptr;
SetCallback(callback):
UserCallback=callback
SetCrashCallbak(callback):
UserCrashCallback = callback
init(conf) :
Device = &conf.monitor.adb.adb_device;
Program = &conf.monitor.adb.adb_program;
Filter = &conf.monitor.adb.adb_filter; = « »
SubSystem = &conf.monitor.adb.adb_sub_system;
enable = &conf.monitor.enable;
MagicWords = &conf.monitor.adb.adb_magic_words;
return init();
1
1
2
2
3
3
4
Monitor initialisation
2
2
3
4
4
init() :
return init(*Device, *Program, *Filter, *SubSystem);
Init(string &device, string &program, string &filter, string &subsystem):
ADBProcess.setup("3rd-party/adb/adb», ADBCallback(bytes, n))

## Slide 2
5g_fuzzer
Config &conf = StateMachine.config;
…
Monitors MonitorTarget = new Monitors();
…
If(MonitorTarget.setup(conf)){
MonitorTarget.SetCallback(log_monitor_program_str);
MonitorTarget.SetCrashCallback(monitor_crash_callback);
MonitorTarget.init(conf);
MonitorTarget.printStatus();
}
…
log_monitor_program_str : only fancy log setup
monitor_crash_callback() : AnomalyReport.IndicateCrash(format("[Crash] Crash detected at state \"{}\"", StateMachine.GetCurrentStateName()));
5gnr_gnb_config.json
"Monitor": {
"Enable": true,
"PrintToStdout": true,
"WaitExternalEvent": false,
"ActiveMonitorTypes": [
3 (only corresponds to ADB used in switch)
],…
"ADB": {
"ADBDevice": "UWEUW4XG8XCA8PWS",
"ADBFilter": "",
"ADBMagicWords": [
"ModemEvent: modem_failure",
"ModemRestartStats",
"SOC crashed",
"Unable to wake SOC"
],
"ADBProgram": "logcat",
"ADBSubSystem": "radio,crash,system,main"
}
Monitors.hpp
setup(conf):
If ADB new MonitorADB();
SetCallback(log_monitor_program_str);
SetCrashCallback(monitor_crash_callback);
init(conf);
printStatus();
customADB
Monitor execution
Executed in background
MonitorADB.hpp
ADBCallbak(char* bytes, size n):
buffer = string(bytes)
If buffer.contains(MagicWords):
UserCrashCallback()
vector<string> lines;
strtk::parse(adb_buffer, "\n", lines);
UserCallback(lines)

## Slide 3
5g_fuzzer
NRPacketLogger.SetPostLogCallback([&](const string msg, bool error) {
if (conf.options.live_protocol_capture)
WSPacketLogger.writeLog(msg, error);
})
5gnr_gnb_config.json
"Monitor": {
"Enable": true,
"PrintToStdout": true,
"WaitExternalEvent": false,
"ActiveMonitorTypes": [
3 (only corresponds to ADB used in switch)
],…
"ADB": {
"ADBDevice": "UWEUW4XG8XCA8PWS",
"ADBFilter": "",
"ADBMagicWords": [
"ModemEvent: modem_failure",
"ModemRestartStats",
"SOC crashed",
"Unable to wake SOC"
],
"ADBProgram": "logcat",
"ADBSubSystem": "radio,crash,system,main"
}
Monitors.hpp
setup(conf):
If ADB new MonitorADB();
SetCallback(log_monitor_program_str);
SetCrashCallback(monitor_crash_callback);
init(conf);
printStatus();
customADB
Crash Logging
Executed in background
MonitorADB.hpp
ADBCallbak(char* bytes, size n):
buffer = string(bytes)
If buffer.contains(MagicWords):
UserCrashCallback()
vector<string> lines;
strtk::parse(adb_buffer, "\n", lines);
UserCallback(lines)
PacketLogger.hpp
writeLog:
Msg = PacketData
_PacketData[4] = 0xA;
if (error)
_PacketData[5] = 0xFA;
else
_PacketData[5] = 0xFC;
1
2
3
Future modifications :
We would like to have the corresponding MagicWord into the wireshark capture : is msg parameter holding the correct string ?
Interesting thing : for a crash, sometimes the value in the packet is 0xFC or 0xFA and both seem to be errors.
output.pcap
Add the corresponding packet