## Slide 1: FLIGHT TEST INSTRUMENTATION DIANE
At the heart of embedded telemetry installation
Data concentrator for collection, processing and formatting for telemeter or recorder
Spy all data or parse in real-time
Embedded storage
Data recording: digital, analog
Software for:
  setup,
  data conditioning,
  data processing,
  data counting
  maintenance.
Platform for recording, telemetry, output IENA.
Embedded on | RAFALE, MIRAGE, ATL2, FALCON, NEURON
Several kind of IO | 1553B, 3910, DGBS,A429, CCE,CAN,PCM, LS, ethernet, various sensors, audio/video.

## Slide 2: FLIGHT TEST INSTRUMENTATION DIANE
 | 8 slots version (9.5 dm3) | 5 slots version (7.5 dm3)
Size (L*H*P) | 202 x 152 x 314 mm | 124 x 194 x 314 mm
Weight | < 10Kg | < 6Kg
Time frame | 10µs | 10µs
Digibuses | Channels | Comments
Digibus | 2 | GAMT101
1553B | 4 | MIL STD 1553 B
3910 | 1 | STANAG 3910
Serial links | 8 | RS232 / RS422
PCM | N/A | Telemetry
CCE | 3 | 
ARINC | 16 | 429
Manchester | 4 | M88-BTM-IPS-UMP33
CAN | 4 | SAEJ 1939
TOR/ frequency | N/A | Isolated inputs